## Slide 1
A dedicated eRHIC
Detector Design
(RICH-related part of the DIS 2016 talk)
Alexander Kiselev
BNL EIC taskforce meeting
April 28, 2016

## Slide 2: BeAST detector layout
hadronic calorimeters
RICH detectors
silicon trackers
GEM trackers
3T solenoid cryostat
-3.5 < h < 3.5: Tracking & e/m Calorimetry (hermetic coverage)
magnet yoke
9.0m
Micromegas barrels
TPC
e/m calorimeters
hadrons
electrons

## Slide 3: Superconducting solenoid
Implement in the same compact design:
homogeneous ~3T field in the TPC
hadron-track-aligned field in the RICH
Keep it simple (no dual solenoid configuration; no reversed current coils; no flux return through HCal; no warm coils between RICH and EmCal)
Central field | 3T
Current density | 23 A/mm2
Full current | 4.6 kA
Main coil radius | 1500 mm
Coil pack length | 3520 mm
Cryostat inner radius | 1350 mm
+/- 4% or so
h = 1.0
h = 1.5
RICH
location
Goal:
Field variation in TPC volume
TPC volume
h = 3.5

## Slide 4: Will gas radiator RICH work in this field?
EIC R&D project
Realistic solenoid magnetic field
Realistic tracker momentum resolution
Cerenkov angle smearing in the field
CsI quantum efficiency e(l) dependence
Refractive index n(l) variation
Finite readout board “pixel” size
ROOT TMVA-based output evaluation
1m long CF4 gas volume [1.5 .. 2.5]m from the IP
1m focal length; ~33mm ring radius at b ~ 1
GEM readout; effective 2.5mm hexagonal pads
Assume on average 12 photons per ring at b ~ 1
Additional 300 mrad instrumental resolution
Consider configuration inspired by the RD6 test run:
“Back-of-the-envelope” Monte-Carlo study:
NB: this spread is in principle noticeable compared to the intrinsic single-photon angular resolution of ~1 mrad
Expected magnetic field effect

## Slide 5: Relative pion/kaon/proton yields
20x250 GeV configuration; yields versus momentum in the 4 < h < 4 range:
p/K/p distributions at the same h look similar
p/K ratio is about 3:1 -> depending on the desired efficiency and contamination this defines the required suppression factors

## Slide 6: Gas radiator RICH in the magnetic field
Require 95% kaon positive identification efficiency
But we do not expect any SIDIS hadrons there:
So yes, RICH with a long enough gas radiator should work just fine in this solenoid stray field
worsening momentum resolution at h ~ 3.5 is what matters here
… and magnetic field plays a role only at very
high momenta and at pseudo-rapidity ~ 1

## Slide 7
3cm thick aerogel; 20cm expansion volume
<n0> = 1.05
~5cm attenuation length
SiPM array readout; 5mm2 “pixel” size
Assume on average 15 photons per ring at b ~ 1
Will aerogel RICH work in such a field?
Consider end-cap case in proximity-focusing configuration:
“Back-of-the-envelope” Monte-Carlo study:
Constant Bz ~ 3T
Asymmetric (f-dependent) attenuation
f-dependent Cerenkov angle smearing in the field
SiPM quantum efficiency e(l) dependence
Refractive index n(l) variation
Emission point uncertainty (thick radiator)
Finite readout board “pixel” size
TMVA-based output evaluation
NB: at 3T full track bending in aerogel volume is >5 mrad at 5 GeV/c!
Require 95% kaon positive identification efficiency
Aerogel RICH R&D for Belle II upgrade
… and magnetic field is again a minor effect